## Slide 1: SPESIFIKASI & STANDARD SISTEM LAMPU ISYARAT
Ir. NOOR HAFIZA BT NOOR KASSIM
KURSUS REKABENTUK SISTEM LAMPU ISYARAT CKE, JKR 26 Julai 2021

## Slide 2: SPESIFIKASI
JKR/SPJ/2008-S8 : Section 8 Traffic Signal System
L-S1 : Specification For Low Voltage Internal Electrical Installation
L-S3 : Specification For Low Voltage Underground Cables

## Slide 3: JKR/SPJ/2008-S8 : Section 8 Traffic Signal System
General
Low voltage underground cables
Signal lanterns/ heads
Signal post/poles and mast arm
Pedestrian push buttons
Traffic controller
Vehicle detectors
Road works

## Slide 4: Section 2 : Low Voltage Underground Cables
Power Cables : PVC/SWA/PVC
Feeder Cables for Vehicle Detectors : PVC/SWA/PVC
Loop Cables : Inductive vehicle loop detector
Latest : Flourinated Ethylane Propylene (FEP) insulated Cu Loop detector cable, 20 SWG, 18 nos stranded, 0.18mm Dia, 0.25m Protection Thickness with FT 1 flammability, low friction, heat & chemical and UV resistance

## Slide 5: Section 2 : Low Voltage Underground Cables
Earthing system
  Earthing conductor shall be 25mm x 3mm copper tape
  Earth electrode shall be copper jacketed steel core rods with 16mm diameter 1500mm length ( each earth electrode is driven 3000mm)
  Earth chamber heavy duty pre-cast concrete of minimum 300mm (L) x 300mm (W) x 210mm (H) complete with removable concrete cover
Cable Pit : Precast concrete pit 450mm (L) x 450mm (W) x 450mm (H)
Detector Pit : Precast concrete pit 300mm (L) x 300mm (W) x 300mm (H)

## Slide 6: Section 2 : Low Voltage Underground Cables
Cable termination
  all cable termination and jointing works shall be carried out in the presence of the S.O
  Power, feeder and loop cables shall be terminated as LS-3
  Loop cables shall be terminated using appropriate cable connector
  cables between poles, loop detectors and traffic signal controller shall be fully installed in galvanized steel pipes and cable pits. The galvanized steel pipes shall be of heavy duty type,

## Slide 7: Section 3 : Signal Lanterns/Heads
Nominal diameter : 300mm
Three optical system : Red, Amber and Green
Height of signal head :
  For drivers / Pedestrian : Centre of Green optical is 2.5m above carriageway level
  Overhead Pole : Lowest point signal head 5.5m not more than 6.5m

## Slide 8: Section 3 : Signal Lanterns/Heads
Lamp
  Halogen lamp used in the optical system shall be a 10 V, 50W, long life tungsten halogen lamp
  LED Hi-Flux : 12W – 15W (Typical 12W)
  LED ultra bright type rated for 100,000 hours of continuous operation from -15°C to + 60°C
  LED module minimum useful life of 48 months

## Slide 9: Section 3 : Signal Lanterns/Heads
Digital countdown unit
  shall consist of a double digit display made of Red and Green LEDs
  Timing is derived directly from controller using Vehicle Actuated Data and no timing shall be programmed
  Each unit shall have the manufacturer's name, trademark, model number, serial number, date of manufacture (month-year), and lot number as identification permanently marked on the back of the module.
  rated voltage and power shall be permanently marked on the back of the module

## Slide 10: Section 4 : Signal Post/Poles and Mast Arms
signal posts / poles, signal mast arms and mountings of signal lanterns / heads shall be shown as in drawings
signal posts shall be of tubular hollow section of steel with a nominal diameter of 100mm
fitted with a weather-proof cap to prevent ingress of water
posts and mast arms shall be capable of having holes drilled in the vertical section, 1m above the ground, for the mounting of one pedestrian push-button

## Slide 11: Section 5 : Pedestrian Push Buttons
push-button detectors shall be provided facing the footpath at each end of each crosswalk
push button is pressed, an internally illuminated panel shall light up bearing a symbolic red standing man. It shall continue to be displayed until the cross signal (green man) commences.

## Slide 12: Section 6 : Traffic Controller
Weatherproof cabinet Class IP55
microprocessor-based consisting of a micro processing unit, interfacing unit for inputs and outputs
controller shall be able to provide eight signal groups of control and shall be capable of expansion to at least sixteen signal groups by the addition of modules on site, which shall be in addition to any special phase required

## Slide 13: Section 6 : Traffic Controller
Housing
  shall have a weatherproof enclosure for the protection of power supplies, kWH meter panel, mains supply panel, facility switch, logic module, vehicle detectors, interfacing and lamp switching modules and battery back-up mains supply system (if specified).
  shall be manufactured from aluminium, stainless steel SS316, electro galvanized steel or mild steel material
  shall be coated with epoxy dry-powder and oven baked semi-gloss enamel grey except for stainless steel
  shall be bolted to steel channel base on concrete plinth
  Appropriate entry and support for cables shall be provided
  metal bracket bar with pad lock shall be installed to hold the controller housing. A log book shall be provided and attached to the housing.

## Slide 14: Section 6 : Traffic Controller
Controller Mains Supply Panel
  shall include one number of single pole miniature circuit breaker (MCB) of minimum rated current 30A
  Tinned copper earthing bar of cross sectional area not less than 25mm x 6mm
  SPD or isolation transformer shall be install

## Slide 15: STANDARD DRAWINGS
Standard Drawings For Road Works STD DRW/S8 (PINDAAN 2014) Section 8 : Traffic Signal System
Standard Traffic Signal Head
Standard Pedestrian Signal Head
Signal Head Details
Feeder Pillar / Controller Housing
Details of Feeder Pillar / Controller
Traffic Signal Column (Tubular Hollow Type – Side Hinge)

## Slide 16: STANDARD DRAWINGS
Standard Drawings For Road Works STD DRW/S8 (PINDAAN 2014) Section 8 : Traffic Signal System
Traffic Signal Column (Tubular Hollow Type – Top Hinge)
Traffic Signal Column (Overhead Type )
Octagonal Tapered Joint Used Mast Arm Column (No Arm Type)
Octagonal Tapered Joint Used Mast Arm Column (With Arm Type)
Traffic Signal Head Mounted On Road Lighting Column (No Arm Type)
Traffic Signal Head Mounted On Road Lighting Column (With Arm Type)
Traffic Signal Information Board

## Slide 17: LAIN LAIN RUJUKAN
ATJ 13/87 (PINDAAN 2017)
A GUIDE TO THE DESIGN OF TRAFFIC SIGNAL